## Slide 1: IoT Alarm system with bed presence detection

## Slide 2: Project’s Architecture
- Hardware components
- Data Proxy Server
- Time-series database
- Data-Analysis module
- Grafana Dashboard
- Data-evaluation module

## Slide 3: Hardware components
ESP32
Pressure Sensor
MP3 TF-ID
Speaker

## Slide 4: Software implementation
The software was implemented using the Arduino IDE.
Several libraries were used:
SoftwareSerial.h
DFRobotDFPlayerMini.h
Wifi.h
PubSubClient.h
HTTPClient.h

## Slide 5: Threshold configuration
Threshold can give rise to many false positives.
A simple threshold selection pipeline was followed:
Put the pressure sensor under the bed.
Check the value in an idle state.
Check the value with a person on it.
Decide a reasonable value between the two boundaries.

## Slide 6: Data proxy server
Core component of the application, manages both the user and device interactions all via HTTP requests.
User list of commands:
set_time
set_sleeping_hours
set_threshold
set_days
sampling_rate
stop_alarm
show_variables
ESP32 list of commands:
alarm_stopped
data
time

## Slide 7: Data proxy server - MQTT
Interactions with ESP32 is bidirectional, the server uses an MQTT broker to send data to the device.
ESP32 subscribed topics:
esp32/commands/stop_alarm
esp32/commands/trigger_alarm
esp32/commands/sampling_rate

## Slide 8: Data proxy server - InfluxDB
Also handles tranmission of device data to the time-series database.
After the time command is received.

## Slide 9: Data analysis module
Takes as input four parameters:
start_date
start_time
end_date
end_time
Computes sleep time and mean latency between those dates

## Slide 10: Grafana Dashboard
Used to display metrics and the average sleeping time

## Slide 11: Data evaluation module
Used to compute accuracy, precision, recall as well as precision-recall curves.

## Slide 12: Thanks for the attention!